## Slide 1
Electricity
Objectives:
Batteries, Electromotive Force
Electric Force and Charges
Electric Current and Ohm’s Law
Electric Power
Electric Circuits

## Slide 2
Electric Force and Charge
Negative
Positive
Electric Charge
+
-
Electric Force
+
+
-
-
-
+
Repulsion
Repulsion
Attraction
Electron
-
- 1 e
Proton
+
+ 1 e
1 e: Smallest amount of charge on a separate object

## Slide 3
Neutral
Atoms
Positive Ions
Electronegativity:
Atoms and Ions
How strongly atoms hold to their electrons
High
It takes more energy to separate an electron. More difficult to convert into positive ion
Low
It takes less energy to separate an electron. Easier to convert into positive ion
Q. Of Cu (copper, 1.90) and Zn (zinc, 1.65), which will require less energy to convert: Cu -> Cu2+ or Zn -> Zn2+
Number of electrons are equal to that of protons. Positive and Negative Balance!
Missing Electrons, Positive is more than Negative
Negative Ions
Missing Electrons, Positive is more than Negative

## Slide 4
Daniell’s Cell
!!! It costs less energy to create Zn2+ ions than Cu2+ ions !!!
Zn on left electrode and Zn2+ ions in solution are in balance.
Cu on right electrode and Cu2+ ions in solution are in balance.
Negative Zn side: Too many Zn2+. Their corresponding electrons will remain on Zn plate
Voltage: 1.1 V
Positive Cu side: Too few Cu2+. That side will be happy to attract electrons to convert its neutral Cu into Cu2+

## Slide 5
1.5 V
1.5 V
Electromotive Force
Electromotive Force/Pressure
Work to move one charge
[Volts]
Q. How much is the E when you connect in parallel?
Q. How can you create 3.0 V with 1.5-V battery?
1.5 V
1.5 V
1.5 V
1.5 V
Ans. 1.5 V
E
Q. How much is the E ?
1.5 V
Ans. 0 V

## Slide 6
Lead-Acid Battery
Lead – Acid Battery: Electrochemical reaction between the Lead and Lead Dioxide electrodes, and sulfuric acid
Q. How many volts does a car battery produces?
Q. How many Daniell’s cells do we need for that?
Voltage: 2.0 V

## Slide 7
Dry Cell Batteries
Carbon – Zinc: 1.5 V
Liquid-filled batteries are not practical sometimes. We need a “dry” cell.
Alkaline: 1.35 V (mercury-based) or 1.5 V (silver oxide type)
Question: How are the 9.0 V batteries produced?
Ans. 6 tiny carbon-zinc or alkaline batteries in series.

## Slide 8
Rechargeable Batteries
Nickel - Cadmium
Lithium
Can be recharged many times
Natural Voltage of 1.2 V (Less than the 1.5 V of the previous batteries
They have “memory”: they loose their efficiency when discharged past the point they are usually discharged
Cadmium is toxic!
Can be recharged many times
Natural Voltage: 2.50 V !
Very light (Li is light) – great for watches, cameras, etc.

## Slide 9
Electric Current
Electric Current
Amount of positive charges flowing every second
[Ampere] or [A]
+
1.5 V
+
-
I
Q. Safe or unsafe?
Note: Physically, it is the negative charges that move!
 | (a) Safe | (b)Unsafe | (c) Uhhh
1.0 A |  |  | 
1.0 mA |  |  | 
1.0 µA |  |  | 

## Slide 10
Ohm’s Law
Electric Current through is directly proportional to the Electromotive Force (Pressure)
+
1.5 V
+
-
I
I
=
E
R
E
Resistance
R
Ohm [Ω]
Q. How much is the current generated by 1.5 V through a 6.0-kΩ resistor (load)?
I
=
E
R
=
1.5
6000
= 0.25 mA

## Slide 11
Power
I
=
E
P
+
1.5 V
+
-
I
E
Q. How much power is dissipated in the load if E=2.0 V
and I = 0.5 A?
Ans. 1.0 W
Watts: How many Joules every second
Q. How much power is dissipated in 2.0-kΩ load if E=2.0?
Ans. 2.0 mW
I
=
E
P
(0.5 A)
=
(2.0 V)
P
2
R
=
E
P
2
R
=
I
P

## Slide 12
Ohm’s Law; Power
20
P1. If you double the voltage, what happens to the current through the load?
Ans.
P2. 1.2-mA current goes through a 50-kΩ load. What is E?
Ans.
Ans.
P3. The resistance of a human is approximately 1.0 MΩ. How much will be the current if you hold the terminals of a 9.0-V battery.
Ans.
P4. A 200-W light bulb is connected to the electrical outlet. How much is the current through it?
P5. A 20-kΩ load is connect to a 20.0-V battery. How much is the power?
Ans.
P6*. A 20-kΩ load is connect to a 20.0-V battery. How much energy does it consume in 1 min?

## Slide 13
Electric Circuits in Series
R1
+
R2
=
Total Resistance
+
R3
+
…
R1
R2

## Slide 14
Electric Circuits in Series
Q. How much is the resistance in the circuit?
Ans. 1.125 Amp
3.0 Ω
+
5.0 Ω
=
8.0 Ω
R1
+
R2
=
Total Resistance
+
R3
+
…
Q. How much is the current in the circuit?

## Slide 15
R1
+
R2
=
Total Resistance
+
R3
+
…
1
1
1
1
R1
R2
Electric Circuits in Parallel

## Slide 16
Q. How much is the resistance in the circuit?
Ans. 3.15 Amp
R1
+
R2
=
Total Resistance
+
R3
+
…
Q. How much is the current in the circuit?
1
1
1
1
4.0
+
10.0
1
1
=
Rtotal
1
0.25
+
0.1
=
Rtotal
1
Rtotal
0.35
=
1
Rtotal
2.86 Ω
=
Electric Circuits in Parallel

## Slide 17
Circuits in Series and Parallel
20
P1. Find the series elements
P3. Find the parallel elements
P2. Find the resistance of the series elements
P4. Find the resistance of the parallel elements